## Slide 1: Platforms: Lecture 10: External Buses

## Slide 2: IDE/ATA
Nominally called the IDE (Integrated Drive Electronics) bus; how ever it's more correctly known as the ATA (Advanced Technology Attachment) specification [ATA Bus].
Used in PCs as a hard-drive or peripheral bus to interconnect the PC mother board and a hard drive.
The IDE bus is a Parallel bus: 16 bits at once
With the introduction of the SATA specification, Parallel ATA [IDE] is now being called PATA
The specification has been upgraded a number of times
Each new version of the standard produced an increase in bus speed.
The maximum IDE bus speed is 133MBytes/sec [133MBps].

## Slide 3: IDE/ATA motherboard connector
On older machines usually two connectors IDE1 and IDE2
Each can control two devices: typically HDD, DVD or CD drives

## Slide 4: IDE/ATA motherboard connector

## Slide 5: IDE/ATA examples
ATA-2 (EIDE, or Fast ATA), [Obsolete] 16.6MBytes/sec, 8 or 16 bit data width, 40 pin data ribbon cable/connector
ATA-7 Ultra-ATA/133, 133MBytes/sec,16 bit data width/40 pin data connector/80 pin cable,
  additional 40 new pins are Ground
ATAPI (ATA Packet Interface) is the CD-ROM side of the interface. Same connector as ATA, +1 extra for analog and +1 for digital audio

## Slide 6: IDE/ATA Interface
ATA-# interface for disk drives; defines the Physical layer, Electrical layer and Signalling protocol
The hard drive, computer, and software determine the mode used: Programmed Input/Output (PIO) or Direct Memory Access (DMA).
Addressing on the bus is defined by the HDD: CHS (Cylinder, Head, Sector)

## Slide 7: SATA
SATA sends a bit at a time
  (cf. PATA sends 16 bits at once)
Uses a 4 conductor cable with two differential pairs [Tx/Rx], plus an additional three ground pins and a separate power pin.
Data runs at 150MBps [1.5GHz] using 8B/10B encoding and 250mV signal swings

## Slide 8: SATA Motherboard Controller
Here six SATA II connectors

## Slide 9: 8B/10B Encoding and SATA versions
each 8 bit data byte is translated into a 10 bit character in order to equalize the numbers of 1's and 0's sent
this achieve DC-balance and bounded disparity, and yet provide enough state changes to allow reasonable clock recovery.
the encoded signal also contains an embedded clock.
SATA-1 Data runs at 1.5Gbps using 8B/10B encoding and 250mV signal swings
Latest SATA 3.2 runs at 16Gbps transfer rate

## Slide 10: SATA Bus Protocol Frame
Used between host and device
SO: . Start-of-frame
FIS: Frame Information Structure
CRC: Cyclic Redundancy Code
  SATA uses a 32bit CRC (calculated over the contents of the FIS)
EOF: End-of-Frame

## Slide 11: PCI
Peripheral Component Interface 'PCI' Bus
  originally developed as a local bus expansion for the PC (ISA) bus
PCI(original): 32 bit bus @ 33MHz (133MB/s)
PCI-X: 64 bit bus@ 133MHz (1064MB/s)
  i.e. transferring either 32 or 64 bits of parallel data on each clock ‘tick’

## Slide 12: PCI Expansion Card
Here as a network card
PCI cards also for
  modem, graphics card (older computers), scanner, sound card, game controller

## Slide 13: PCI Motherboard Connectors
Here are two (white) PCI connectors

## Slide 14: PCI Bus
(64bit) PCI bus is made up of the following (major) signals:
Address/Data Bus: 64bit Address; 64bit Data, (Time Multiplexed)
System Bus: 2 bits; (Clock/Reset)
Interface Control Bus: 7bits; (Ready, Acknowledge, Stop).
Parity Bus: 2 bits (1 for the 32 LSBs and 1 for the 32 MSB bits)
Errors Bus: 2 bits, (1 for Parity and 1 for System)
Command/Byte Enable: 8 bits (0-3@32bit, and 4-7@ 64bit Bus)
64MHz Control: 6 bits; (2-Enable/Running), (2-Present), (2-Ack/Req)
Cache: 2 Bits, Interrupt bus: 4 bits, JTAG Bus: 5 bits
Power: +5, +3.3, +12, -12v, GND

## Slide 15: AGP
The Accelerated Graphics Port
  a Video Local bus
derived from the PCI bus but with 20 additional signals
The PCI-Express card bus has replaced the AGP bus
Right an AGP expansion card

## Slide 16: AGP Motherboard connector
The specification increased from 1x to 8x speeds
AGP 3.0 8x: Rate = 2.133GB/s
Dark brown AGP - now only seen in older computers

## Slide 17: PCI Express (PCIe)
PCI Express specification :
  a point to point serial interface over copper wire or optical fibre.
The link is two low-voltage differential pairs of wires, at 2.5Gb/s in each direction [one transmit, and one receive pair].
  Overall rate of 16 Gb/s
PCI Express uses 8B/10B encoding
  each 8 bit byte is translated into a 10 bit character in order to equalize the numbers of 1's and 0's sent, and the encoded signal contains an embedded clock.

## Slide 18: PCIe
On a motherboard
  x1 PCIe slot will support a bandwidth of 5Gbps (used as a usual expansion card slot)
  x16 PCIe slot will support 80Gbps (used as video card expansion slot)
PCIe connectors & busses are NOT compatible with PCI
  At the software level they are compatible. Legacy applications and OS can use PCIe as though PCI, without using it’s newer features.

## Slide 19: PCIe Card
Here a x1 PCIe (driving two SATA2 (3Gb/s) port) LaCie

## Slide 20: PCIe motherboard connectors
One x1 PCIe and one x16 PCIe

## Slide 21: PCIe Types

## Slide 22: PCIe Protocol
1-byte Start-of-Frame
2-byte Sequence Number
16 or 20-byte Header
0 to 4096-byte Data field (size depending on data !)
4-byte ECRC field, & 4-byte LCRC
  End-to-end CRC; local CRC
1-byte End-of Frame.
At best: 4096 bits of data in a total frame of 4124 bits
  i.e. 192 bits of non-data are always transmitted

## Slide 23: Bus Connector Comparisons

## Slide 24: Firewire Bus: IEEE 1394
High performance serial bus
Devices on the bus are Hot-Swappable.
supports up to 63 devices at a maximum cable distance between devices of 4.5 meters.
The maximum devices on the bus is 16 allowing a total maximum cable distance of 72 meters.
The digital interface supports either asynchronous and isochronous data transfers.
Addressing is used to a particular device on the bus. Each device determines its own address.

## Slide 25: Firewire Bus: IEEE 1394
Network-like characteristics
Device controllers independent

## Slide 26: Firewire Data Speeds
UTP cable over 100m distance
  Over Fibre cable over CAT5 UTP cable up to 100Mbps [1394a] Half-duplex Manchester encoding
  over CAT5 cable up to 800Mbps [1394b]. Full duplex and 8B/10B encoding
  Over CAT5(but better Cat5e or 6) cable up to1600Mbps [1394c] Gigabit Ethernet or 1000Base-T
at 1Gb/s: (Distance depends on the fibre):
  plastic MM fibre – 550m
  SM fibre – up 10km
  SM fibre (@1550nm) - ~ 70km

## Slide 27: Firewire Connector
Different types of 1394 connectors, usually mounted on a bracket, which is then cable connected to a header on the motherboard
IEEE1394 headers on motherboard
Two types of IEEE1394 output connectors
(mini DV + 6-pin connector )
on bracket

## Slide 28: USB
Root
Hub
Hub
Hub
Hub
USB defines 2 types of hardware: Hub and Device.
Up to 127 devices may be connected together in a tiered Star topology - the limiting factor being 7 address bits.
The physical wire segments are point-to-point between a Host, Hub, or Device.
The system may only have one Host, which connects to a Hub (or to a single device).
A USB Hub may connect to another Hub or to a USB device – Hubs provide multiple connection points for devices.

## Slide 29: USB
USB cable connector/plug type A
USB cable connector/plug type B

## Slide 30: USB
A USB port supplies 5V
Unit load defined as 100mA USB 2.0 (150mA USB 3.0).
A maximum of 5 unit loads can be drawn from a port in USB 2.0 ( 6 in USB 3.0)
2 types of device: low-power and high-power.
  Low-power devices draw at most 1 unit load (100mA)
  High-power devices draw (up to) the maximum number of unit loads supported by the standard (500mA)
All devices default as low-power but the device's software may request high-power as long as the power is available on the providing bus.
Non-Standard devices
  External hard drives: use one cable/port for data and power + one cable/port for power only
  Non-communicating devices: lights, vacuum cleaners, battery chargers: take power only

## Slide 31: USB / Firewire similarities
Both serial, multipoint bus specifications
Add/remove devices w/o powering down
Packet protocol for isochronous data transfer
  Isochronous: delivery at regular time intervals
  Guarantee specified throughput

## Slide 32: USB / Firewire differences
USB: slow to medium speed data transfer applications, i.e., storage devices
  12 Mbits/sec
USB-2: high-speed data transfer
  480Mbits/sec
USB-3 (SuperSpeed USB )
  4.8Gbits/sec
FireWire: high-speed data transfer, i.e., full motion video with sound
  400 Mbits/sec to 3.2 Gbits/sec

## Slide 33: USB / Firewire differences
USB 1.0 and 2.0 use a "speak-when-spoken-to" protocol; peripherals cannot communicate with the host unless the host specifically requests communication. (USB 3.0 allows for device-initiated communications towards the host ).
A FireWire device can communicate with any other node at any time, subject to network conditions.
A USB network relies on a single host at the top of the tree to control the network.
In a FireWire network, any capable node can control the network.
USB runs with a 5V power line, while Firewire can supply up to 30V.

## Slide 34: SCSI
Small Computer System Interface
Multiple variations to the original ANSI standard
Really an I/O bus rather than simple interface
  Supports multiple devices from a single SCSI port

## Slide 35: And more connectors
Mini-USB for smartphones, ereaders etc.
Various Lightning and earlier connectors for iPads etc