## Slide 1: Platforms: Lecture 8: Peripherals

## Slide 2: What is a peripheral?
Devices that are separate from the basic computer
  Not the CPU, memory, power supply
Classified as input, output, and storage
Connect via
  Ports: parallel, USB1.0 (1.5Mb/s), USB1.1 (12 Mb/s), USB2.0 (480Mb/s), USB3.0 (4 Gb/s), serial
  Interface to systems busses: SCSI (Small Computer Systems Interface), IDE (Integrated Drive Electronics, WD) - ATA, ATAPI; PATA, SATA, PCMCIA (Personal Computer Memory Card International Association)
Many slides using pictures from Englander (2003) and Silberschatz (2005)

## Slide 3: Storage Devices
Primary memory
  Data and programs must be copied to primary memory for CPU access
Secondary storage
  Permanence of data
  Direct access storage devices (DASDs)
  Online storage
  Offline storage – loaded when needed
Speed
  Measured by access time and data transfer rate
  Access time: average time it takes a computer to locate data and read it
  Data transfer rate: amount of data that moves per second

## Slide 4: Hierarchy of Storage

## Slide 5: Secondary Storage Devices
Hard drives, floppy drives
CD-ROM and DVD-ROM drives
CD-R, CD-RW, DVD-RAM, DVD-RW
Tape drives
Network drives
Direct access vs. Sequential access
Rotation vs. Linear

## Slide 6: Magnetic Disks 1
Magnetic disks provide bulk of secondary storage of modern computers
Disks can be removable
Drive attached to computer via I/O bus
  Busses vary, including EIDE, ATA, SATA, USB, Fibre Channel, SCSI
  Host controller in computer uses bus to talk to disk controller built into drive or storage array
Notes: SCSI – Small Computer Systems Interface
IDE (Integrated Drive Electronics, WD) – ATA, ATAPI; PATA, SATA
PCMCIA - Personal Computer Memory Card International Association
EIDE – Enhanced IDE
eSATA – External SATA
ISA – Industry Standard Architecture from XT 8 bit, 16 bit AT, no mix
PCI – Peripheral Component Interface, 32/64 bit
PCI Express – serial, faster
AGP- Advanced Graphics Port, now bowing to PCIe

## Slide 7: Magnetic Disks 2
Track – circle
Cylinder – same track on all platters
Block – small arc of a track
Sector – pie-shaped part of a platter
Head – reads data off the disk
Number of bits on each track is the same! Denser towards the center.
CAV – constant angular velocity
  Spins the same speed for every track
  Hard drives – typical 7200 rpm, also slower and up to 15000rpm (or 120 rps up to 250rps)
  Floppy drives – 360 rpm
Head crash results from disk head making contact with the disk surface
    Parked heads

## Slide 8: Hard Disk Layout

## Slide 9: Locating a Block of Data
Average seek time:
  time required to move from one track to another
Latency:
  time required for disk to rotate to beginning of correct sector
Transfer time (or transfer rate):
  time required to transfer a block of data to the disk controller buffer

## Slide 10: Disk Access Times
Avg. Seek time
  average time to move from one track to another
Avg. Latency time
  average time to rotate to the beginning of the sector
  Avg. Latency time = ½ * 1/rotational speed
Transfer time
  1/(# of sectors * rotational speed)
Positioning time (random-access time)
  time to move disk arm to desired cylinder (seek time) plus time for desired sector to rotate under the disk head (rotational latency)
Total Time to access a disk block
  Avg. seek time + avg. latency time + avg. transfer time

## Slide 11: Disk Addressing
Disk drives are addressed as large 1-dimensional arrays of logical blocks, where the logical block is the smallest unit of transfer.
The 1-dimensional array of logical blocks is mapped into the sectors of the disk sequentially.
  Sector 0 is the first sector of the first track on the outermost cylinder.
  Mapping proceeds in order through that track, then the rest of the tracks in that cylinder, and then through the rest of the cylinders from outermost to innermost.

## Slide 12: Disk Management
Low-level formatting, or physical formatting — Dividing a disk into sectors that the disk controller can read and write.
To use a disk to hold files, the operating system still needs to record its own data structures on the disk.
  Partition the disk into one or more groups of cylinders.
  Logical formatting or “making a file system”.

## Slide 13: Magnetic Disks
Data Block Format
  Interblock gap
  Header
  Data
  Formatting disk
Disk Interleaving
Disk Interleaving

## Slide 14: Disk Block Formats
Single Data Block
Header for Windows disk

## Slide 15: Disk Arrays – RAID Structure
RAID (Redundant Array of Independent (Inexpensive) Disks) – multiple disk drives provides reliability via redundancy.
   fault-tolerant computers
RAID is arranged into six different levels.

## Slide 16: RAID (continued)
Several improvements in disk-use techniques involve the use of multiple disks working cooperatively.
Disk striping uses a group of disks as one storage unit.
  when interface can handle data at a faster rate than the disk read/write process for a single disk, striping allows multiple tracks to read/write.
RAID schemes improve performance and improve the reliability of the storage system by storing redundant data.
  Mirroring or shadowing keeps duplicate of each disk.
  Block interleaved parity uses much less redundancy.

## Slide 17: RAID (Levels)
Notes: RAID 0 – striping yes (non-redundant), mirroring no, parity no, no tolerance
RAID 1 – striping no, mirroring yes 1:1, parity no, tolerates all but one drive
RAID 2 – striping yes, mirroring no, parity yes (Hamming Code 1c + 2d),
RAID 3 – striping yes (bit), mirroring no, parity yes, tolerant single drive
RAID 4 – striping yes (block), mirroring no, parity yes, single drive fail
RAID 5 – striping yes, mirroring no, parity yes, tolerant single drive fail
RAID 6 – striping yes, mirroring no, parity yes, tolerant two drives fail

## Slide 18: Alternative Disk Technologies
Removable hard drives
  Disk pack – disk platters are stored in a plastic case that is removable
  Another version includes the disk head and arm assembly in the case
Fixed-head disk drives
  One head per track
  Eliminates the seek time

## Slide 19: Magnetic Tape
Offline storage
Archival purposes
Disaster recovery
Tape Cartridges
  20 – 144 tracks (side by side)
  Read serially (tape backs up)
  Random access ~1000x slower than HDD
  4mm, 8mm DAT , 19mm, LTO-2 and SDLT
  Size 20Gb -200Gb
  typically includes 2:1 compression
Fallen out of significant use

## Slide 20: Optical Storage 1
Reflected light off a mirrored or pitted surface
CD-ROM
  Spiral 3 miles long, containing 15 billion bits!
  Constant Linear Velocity – all blocks are same physical length
  Block – 2352 bytes, of which 2k of data (2048 bytes), 16 bytes for header (12 start, 4 id), 288 bytes for advanced error control
DVD-ROM
  4.7Gb per layer, max 2 layers per side, 2 sides = 17G
Notes: Constant Angular Acceleration (CAA) is a variant of CLV that was used on the Laserdisc format. The initial specification of CLV (as it applied to laserdisc) resulted in several playback artifacts to be present in the audio/video portion as well as compatibility problems with laserdisc players as produced by different manufacturers.
In the mid 1980s, Pioneer Electronics introduced the CAA scheme where the speed in rotation of the laserdisc was lowered in steps and eliminated most playback artifacts and compatibility problems. Since its introduction, most manufacturers of laserdiscs adopted the CAA format but still referred to their CAA-encoded product as CLV.

## Slide 21: Layout CDROM vs Standard Disk
CD-ROM
Hard Disk

## Slide 22: CD-ROMs

## Slide 23: Types of Optical Storage 1
WORM Disks
  Write-once-read-many times
  Medium can be altered by using a medium-powered laser to blister the surface
  Data stored in concentric tracks, sectored like a magnetic disk
Medium-powered laser blister technology also used for
  CD-R, DVD-R, DVD-ROM
  DVD-RAM, DVD+RAM

## Slide 24: Types of Optical Storage 2
CD-RW discs contain a phase-change alloy recording layer composed of a phase change material:
  An infra-red laser beam is used to selectively heat and melt, at 400 degrees (Celsius), the crystallized recording layer into an amorphous state or to anneal it at a lower temperature back to its crystalline state.
  The different reflectance of the resulting areas make them appear like the pits and lands of a prerecorded CD.

## Slide 25: Flash Memory
Flash memory is an electronic non-volatile computer storage medium that can be electrically erased and reprogrammed ( a variant EEPROM, coming in two types named after NAND and NOR logic gates, with NAND type allowing block read/writes, and NOR type allowing word read/writes). Capacity: Mb to many Gb
Limitations of both types include block erasure (if any part of a block is written, entire block must be wiped), memory wear (finite number of program/erase cycles), and in NAND types (read disturb where repeated reads (100,000s) can cause nearby blocks to become programmed)
Wear levelling and preemptive erase as solutions

## Slide 26: Solid State Drives
Flash memory is high-speed, durable, low energy consumption, high capacity, quiet, with no mechanical parts and mechanical latencies.
This has led to emergence of solid-state drives (essentially flash memory as replacement or supplement to standard hard disks)
Retain limitation of memory wear so need wear levelling and defragmentation avoidance
Capacities 128-512 Gb with some high-end drives up to 2 Tb, but 10x more expensive per Gb than hard disks

## Slide 27: Displays
Pixel – picture element
Size: diagonal length of screen
Resolution (pixels on screen)
  VGA: 480 x 640
  SVGA: 600 x 800
  768 x 1024
  1280 x 1024
  1920 x 1080 (HD)
Picture size calculation
  Resolution * bits required to represent number of colors in picture
  Example: 16 color image, 100 pixels by 50 pixels
  4 bits (16 colors) * 100 * 50 = 20,000 bits

## Slide 28: Display Screen
Screen size: measured diagonally
Resolution: minimum identifiable pixel size
Aspect ratio: x pixels to y pixels
  4:3 on most PCs
  16:9 on high definition and widescreen displays

## Slide 29: Colour and Displays
Pixel color is determined by intensity of 3 colors – Red Green Blue or RGB
4 bits per color
  16 x 16 x 16 = 4096 colors
24 bit color (True Color)
  16.7 million colors
Video memory requirements are significant!

## Slide 30: CRTs and Text Monitors
CRTs (similar to old TVs)
  3 stripes of phosphors for each color
  3 separate electron guns for each color
  Strength of beam  brightness of color
  Raster scan (30x per second, Interlaced vs. non-interlaced (progressive scan) )
Text monitors (e.g. simple POS systems)
  24 lines x 80 chars
  A character is the smallest unit on a screen
  Very little memory required
  Fast for remote transmissions

## Slide 31: Interlaced vs Noninterlaced
Interlaced video is a technique of doubling the perceived frame rate introduced with the signal without consuming additional bandwith. With progressive scan or noninterlaced, an image is captured, transmitted, and displayed in a path similar to text on a page: line by line, from top to bottom.

## Slide 32: Diagram of Raster Screen Generation Process

## Slide 33: Display Example

## Slide 34: LCD – Flat Screen
Fluorescent light panel
3 color cells per pixel
Operation
  1st filter polarizes light in a specific direction
  Electric charge rotates molecules in liquid crystal cells proportional to the strength of colors
  Color filters only let through red, green, and blue light
  Final filter lets through the brightness of light proportional to the polarization twist

## Slide 35: LCD Operation

## Slide 36: LCDs (continued)
Active matrix
  One transistor per cell
  More expensive
  Brighter picture
Passive matrix
  One transistor per row or column
  Each cell is lit in succession
  Display is dimmer since pixels are lit less frequently

## Slide 37: Printers
Dots vs. pixels
  300-2400 dpi vs. 70-100 pixels per inch
  Dots are on or off, pixels have intensities
Types
  Typewriter / Daisy wheels – obsolete
  Dot matrix – usually 24 pins, impact printing, esp. for multi-copy printing (line printers), also obsolete
  Inkjet – squirts heated droplets of coloured ink
  Laser – B/W & colour
  Thermal wax transfer
  Dye Sublimation

## Slide 38: Creating a Gray Scale

## Slide 39: Laser Printer Operation 1
Dots of laser light are beamed onto a drum
Drum becomes electrically charged
Drum passes through toner which then sticks to the electrically charged places
Electrically charged paper is fed toward the drum
Toner is transferred from the drum to the paper
The fusing system heats and melts the toner onto the paper
A corona wire resets the electrical charge on the drum

## Slide 40: Laser Printer Operation 2

## Slide 41: Laser Printer Operation 3

## Slide 42: Touchscreen Devices 1
A resistive touchscreen panel comprises several layers, especially two thin, transparent electrically-resistive layers separated by a thin space.
Top touched screen has a coating on the underside surface and beneath it is a similar resistive layer on top of its substrate. One layer has conductive connections along its sides, the other along top and bottom. A voltage is applied to one layer, and sensed by the other.
When a fingertip or stylus tip presses down onto the outer surface, the two layers touch to become connected at that point, leading to it behaving as a pair of voltage dividers, one axis at a time. Pressures position on screen can then be read.
Notes: Resistive touch is used in restaurants, factories and hospitals due to its high resistance to liquids and contaminants. A major benefit of resistive touch technology is its low cost. Additionally, as only sufficient pressure is necessary for the touch to be sensed, they may be used with gloves on, or by using anything rigid as a finger/stylus substitute. Disadvantages include the need to press down, and a risk of damage by sharp objects. Resistive touchscreens also suffer from poorer contrast, due to having additional reflections from the extra layer of material placed over the screen

## Slide 43: Touchscreen Devices 2
A capacitive touchscreen panel consists of an insulator such as glass, coated with a transparent conductor.
Touching the surface with a finger results in a distortion of the screen's electrostatic field, measurable as a change in capacitance. Different technologies may be used to determine the location of the touch. The location is then sent to the controller for processing.
Cannot use a capacitive touchscreen through most types of electrically insulating material, such as gloves (so tablets and smartphones difficult to use in cold weather).
Solutions include a special capacitive stylus, or a special-application glove with conducting thread leading from outside to fingertip

## Slide 44: Other Computer Peripherals
Scanners
  Flatbed, sheet-fed, hand-held
  Light is reflected off the sheet of paper onto strip of detectors
User Input Devices
  Keyboard, mouse, light pens, graphics tablets
Communication Devices
  Telephone modems
  Network devices