## Slide 1: Platforms
Lecture 4B: Microprocessor Design and the ARM

## Slide 2: Microprocessor Design Approaches
Microprocessor design is a series of complex interrelated problems ranging from physical constraints to market forces.
It is an ongoing process of improvement and refinement to make new processors that are smaller, faster, cheaper, and more energy efficient.
New processors are four times faster than the processors of three years ago.

## Slide 3: ARM Past and Present
The first ARM processor was developed on 3-micron technology in 1983-1985.
We will be using the ARM6/7 architecture first developed between 1990-1995 for examples
Today's ARM processors share the same effective and efficient design principles, have many common elements in their implementation, and the same core assembly language as the ARM6/7 architectures.
ARM6/7 makes for easier examples!

## Slide 4: ARM Past and Present
ARM processors are:
  very high performance devices
  share a common architecture
  consume relatively little power
  and are comparatively inexpensive.
ARM processors can be found in:
  digital cameras, games consoles, iPod Nanos
  automotive control, robotic assembly lines
  broadband modems, routers, networking switches
  smart cards and mobile phone SIMs.

## Slide 5: ARM Technical Details
The ARM is a load/store architecture:
  only load and store instructions access memory
  All other instructions are register-to-register
  This speeds up overall operation as register accesses are much faster than memory accesses.
All ARM6/7 instructions are 32 bits wide:
  are subtle variations on the same regular formats
  makes decoding the instructions easier
  simplifies the necessary circuitry
  and speeds up the fetch-decode-execute cycle.

## Slide 6: ARM Technical Details
All input/output peripherals (such as printers, hard drive disks, and the network) are memory-mapped devices.
There is also hardware support for high-bandwidth data transfer.
ARM processors are 32-bit or 64-bit architectures
32-bit architectures can address a maximum of 232 bytes
  or 4 Gigabytes of memory

## Slide 7: ARM Technical Details
Word size is 32 bits
Half-words are 16 bits wide.
Words are aligned on 4-byte boundaries
Half words are aligned on even byte boundaries.

## Slide 8: Programming Languages
High-level languages:
  include C++, MATLAB, Java, Visual BASIC
  are excellent for application programming
  but must be translated for the microprocessor to act on the programs.
Low-level languages (machine code):
  can be directly understood by the appropriate microprocessors.
  can be hexadecimal "op-codes" sequences
  or written as a long sequence of binary 0's and 1's.
  very difficult to write even short programs

## Slide 9: Programming Languages
To make programming easier, software tools known as assemblers are used.
An assembler translates an assembly language program into op-codes that are understood by the microprocessor.
There will be opportunities to try ARM assembly

## Slide 10: Programming Languages
Assembly language programs are more efficient and require less memory than programs in high-level languages.
There is one assembly language instruction for each op-code in the machine code, giving programmers direct control of the microprocessor.
The actual assembly process is normally quick.
The bad news is that writing large programs in assembly language is still difficult.

## Slide 11: Basics of ARM Instructions
ARM has a simple and short operand encoding scheme
  An operand is a value
This facilitates fixed-length instructions and fast decoding.
Most operations are performed on registers.

## Slide 12: Basics of ARM Instructions
ARM applications view memory as a linear sequence of bytes.
Memory is referenced by addresses, with these addresses taking the form of numbers of bytes from the start of memory.
ARM processors can access individual bytes but it is more efficient to access whole words (32 bits for ARM6/7).

## Slide 13: Basics of ARM Instructions
  Word addresses must be correctly aligned: bits 0 and 1 must be zero.
  Words are normally stored in "little endian" format:
  where the low-order byte is stored at the lowest byte address and the high-order byte is stored at the highest byte address.
  ARM processors can be switched to "big endian"

## Slide 14: ARM Instruction Structure
  All ARM instructions have this structural layout:
label <space> opcode <space> operands <space> ; comment
  Each field (label, opcode, operands and comment) must be separated by <space> elements.
  A <space> element can be an actual space character (from your space bar) or a tab.
  If there is no label, there must be a <space> element before the actual instruction
  A semicolon indicates the start of a comment, which is terminated by the end of the line.
  All sections are optional and blank lines will be accepted by the assembler

## Slide 15: Example ARM Assembly Program
  AREA Example, CODE, READONLY ; name
  ENTRY ; marker of 1st executable instruction
  start ; label
  MOV r0, #11 ; put the value 11 in register 0
  MOV r1, #31 ; put the value 31 in register 1
  ADD r0, r0, r1 ; r0 = r0 + r1
  SWI 0x11 ; terminate the program, unneeded
  ; for Rolecks
  END ; marks the end of the file

## Slide 16: Example ARM Assembly Program
Consider the second MOV instruction:
  MOV r1, #31 ; put the value 31 in register 1
  "MOV" is the opcode for loading a value into a register.
  "r1" and "#31" are the operands for this instruction.
  "r1" is the destination register where the value will be placed.
  "#31" is the decimal number 31. Decimal values can be indicated by a preceding "#" or "#d". Hexadecimal numbers are indicated by a preceding "#h"
SWI is a "software interrupt" - when its operand value is "0x11", it exits the program cleanly

## Slide 17: Example ARM Assembly Program
AREA, ENTRY and END are directives.
  Directives are instructions to the assembler. They are not passed on to the actual microprocessor.
  AREA Example, CODE, READONLY
  The AREA directive can be used to specify and name sections of program code or data, (Example)
  The example is a code segment and indicated as such by the CODE identifier.
  It is also declared as READONLY in that the code cannot be altered during its execution.
  A working ARM assembly program must have at least one CODE area.

## Slide 18: Example ARM Assembly Program
ENTRY and END are also directives.
  The ENTRY directive indicates the first instruction that should be executed within an application.
  The complete application can only have one entry point and so only one ENTRY directive need be issued.
  The END directive indicates the end of the application.

## Slide 19: Types of Instruction
ARM assembly language has three broad categories of instruction:
  Data Processing: this includes arithmetic and logical operations, comparison operations and register movement operations;
  Data Movement: these are instructions to load and store data from and to memory;
  Control Flow: these are software interrupts and branch instructions that alter the order of execution.

## Slide 20: Types of Instruction
For ARM6/7 data processing instructions, operands (values) are always 32 bits wide.
The operands are either held in registers or are specified as constants (called literals) in the instruction itself.
The result of a data processing instruction is also a 32 bit datum and is stored in a register.
Most data processing instructions will have three operands, two of which are inputs and one for the result.

## Slide 21: Arithmetic Operations
Example: ADD r0, r1, r2 ; r0 := r1 + r2
  r1 and r2 are the source registers containing the input operands, r0 is the destination register where the result is stored.
  The destination register can be the same as one of the source registers
  ADD r0, r0, r1 is legal and means add the values in r0 and r1 together and place the result in r0.
  This ADD instruction can be used on both unsigned and 2's complement signed numbers.
  It may produce a carry out signal and set overflow bits, but such signals are ignored by default.

## Slide 22: Arithmetic Operations
Available Arithmetic Operations are:
  ADD r0, r1, r2 ; r0 := r1 + r2
  ADC r0, r1, r2 ; r0 := r1 + r2 + C
  SUB r0, r1, r2 ; r0 := r1 - r2
  SBC r0, r1, r2 ; r0 := r1 - r2 + C - 1
  RSB r0, r1, r2 ; r0 := r2 - r1
  RSC r0, r1, r2 ; r0 := r2 - r1 + C – 1
  The ADC, SBC, and RSC instructions use the carry bit (C), which is stored in the Current Program Status Register (see next lecture)

## Slide 23: Arithmetic Operations
  ADC r0, r1, r2 adds the values stored in r1 and r2 and the value of the carry bit, placing the result in r0.
  In the SBC instruction, the carry bit is used to indicate a "borrow", which is unset (set to 0) when a "borrow" is required.
  These instructions are useful in that they allow programmers to perform arithmetic operations on numbers that are larger than 32 bits.
  RSB is shorthand for "reverse subtraction" (and RSC is "reverse subtraction with carry")
  RSB and RSC switch the order of operands for subtraction

## Slide 24: Logical Operations
Logical operations are performed bit by bit on the input operands (values in registers or constants) and the result placed in a destination register.
  Example: AND r0, r1, r2 ; r0 := r1 and r2
  the result bit is 1 if both input bits are 1
  r1: 0101 0011 1010 1111 1101 1010 0110 1011
  r2: 1101 0110 1010 0000 0111 0101 1010 0011
  r0: 0101 0010 1010 0000 0101 0000 0010 0011
AND instructions are useful for "masking" parts of values that you are not interested in currently.

## Slide 25: Logical Operations
Example: ORR r0, r1, r2 ; r0 := r1 or r2
  the result bit is 1 if either input bit is 1 (an OR operation)
  r1: 0101 0011 1010 1111 1101 1010 0110 1011
  r2: 1101 0110 1010 0000 0111 0101 1010 0011
  r0: 1101 0111 1010 1111 1111 1111 1110 1011
ORR instructions are useful for ensuring that certain bits are set.

## Slide 26: Logical Operations
Example: EOR r0, r1, r2 ; r0 := r1 xor r2
  the result bit is set to 1 if one and only one of the inputs bits is 1 (an exclusive OR operation)
  r1: 0101 0011 1010 1111 1101 1010 0110 1011
  r2: 1101 0110 1010 0000 0111 0101 1010 0011
  r0: 1000 0101 0000 1111 1010 1111 1100 1000
EOR instructions can be useful for inverting specific bits.

## Slide 27: Logical Operations
Example: BIC r0, r1, r2 ; r0 := r1 and not r2
  BIC stands for 'bit clear', where every '1' in the second operand clears the corresponding bit in the first:
  r1: 0101 0011 1010 1111 1101 1010 0110 1011
  r2: 1101 0110 1010 0000 0111 0101 1010 0011
  r0: 0000 0001 0000 1111 1000 1010 0100 1000
BIC instructions can be considered as kind of reverse OR, useful for clearing specific bits
  R2: 1111 1111 1111 1111 0000 0000 0000 0000
  clears upper halfword leaving the lower two bytes untouched.

## Slide 28: Register Move Operations
Example: MOV r0, r1 ; r0 := r1
  The MOV instruction loads a value (either a literal or from a source register, e.g. r1) into the destination register (e.g. r0 in this example).
  A MOV instruction that has the same source and destination registers does not do anything! (e.g. MOV r0, r0 )

## Slide 29: Register Move Operations
Example: MVN r0, r1 ; r0 := not r1
  MVN is shorthand for "move negated". The MVN instruction takes a value (literal or from a register), inverts its bits, and puts it in the destination register.
  r1: 1101 0110 1010 0000 0111 0101 1010 0011
  r0: 0010 1001 0101 1111 1000 1010 0101 1100
  The MVN instruction allows a programmer to put a negative value into a register.
  As 2's complement numbers are involved, it is necessary to move one less than the desired value.
Example: MVN r0, #0 ; moves -1 into r0