## Slide 1: Platforms
Lecture 4C: Assembly Language Operations

## Slide 2: Current Program Status Register
CPSR records program and processor state
  This information is recorded by setting or clearing specific bits in the register.
  It is a 32-bit wide register
The top four bits (bits 31, 30, 29, and 28) are the condition code (cc) bits
  These bits are sometimes referred to as "flags".
The lowest 8 bits (bit 7 to bit 0) store information about the processor's own state.
Bits 27 to bit 8 are currently unused in most ARM processors.

## Slide 3: Current Program Status Register
N bit is the "negative flag" and indicates that a value is negative.
Z bit is the "zero flag" and is set when an appropriate instruction produces a zero result.
C bit is the "carry flag" (and also "borrows" (subtractions) and "extends" (from shifts).
V bit is the "overflow flag"
  set if an instruction produces a result that overflows going beyond representable numbers (2's complement signed)

## Slide 4: Comparison Operations
Comparison operations perform arithmetic or logical operations on register values (or literals) and set condition code flags in the CPSR.
The actual result of the underlying arithmetic or logical operation is not stored in any register.
  Example CMP r1, r2 ; set flags per result of r1 - r2
  N =1 if most significant bit of (r1 - r2) is 1, (r2 > r1)
  Z = 1 if (r1 - r2) = 0, i.e. r1 = r2
  C = 1 if r1 and r2 are both unsigned integers AND (r1 < r2)
  V = 1 if r1 and r2 are both signed integers AND (r1 < r2)

## Slide 5: Comparison Operations
Example: CMN r1, r2 ; set flags per result of r1 + r2
CMN (compare negative) determines the flags by performing the equivalent of: operand1 - ( - operand2)
It is useful for comparing register values against small negative numbers (such as -1, which is frequently used to mark the end of a data structure).

## Slide 6: Comparison Operations
Example: TST r1, r2 ; set flags on r1 AND r2
TST (test bits) can determine if one or more bits are set.
The first operand is the value to be tested.
The second operand is the bit mask.
The Z flag will be set if there is a match, otherwise it will be cleared.

## Slide 7: Comparison Operations
Example: TEQ r1, r2 ; set flags on r1 XOR r2
TEQ (test equivalent) instruction is similar to TST
TEQ employs an exclusive-or operation.
It can be used to determine if specific bits in two operands are the same or different.
It does not change the overflow flag, unlike CMP.
TEQ can be used to determine if two values have the same sign.

## Slide 8: Comparison Operations
The CMP, CMN, TST, and TEQ instructions always alter the condition codes.
Other data processing instructions (such as ADD, ADC, SUB, etc.,) can alter the condition codes if they have an "S" suffix.
Example ADDS r0, r1, r2 ; r0 := r1 + r2 ; and adjust flags for ; result placed in r0
A sequence of ADDS and ADCS instructions could be used to add 64-bit or larger numbers together.

## Slide 9: Basic Branches
In a simple program, one instruction follows another and execution is a sequential process.
In more complex programs, processors will need to execute instructions in a different order:
  An iterative process such as a loop where the program executes a series of instructions and then returns to the start of the sequence to repeat the same set of instructions with different values.
  A decision-making process, where a comparison operation is performed, and based on its result, skips over instructions to reach a different program section and continues execution from that point.

## Slide 10: Basic Branches
This movement is called branching, and uses branch (or jump) instructions.
  B label ; branch to the instruction at "label“ ... ... label ...
The B instruction is an unconditional branch.
  When the processor encounters such a branch, it always jumps to the designated point.
The branch destination can be a symbolic label
  assembler converts it into correct memory location

## Slide 11: Conditional Branches
A comparison operation enables decisions to be made; conditional branches allow the computer to act on decisions.
ARM conditional branches are executed (taken) or not depending on the flag bits of the Current Program Status Register (CPSR), e.g.
  BNE (branch not equal) instruction uses the Z bit
  If the Z bit is set (a result was zero or a comparison was equal), then the branch is not taken.
  If the Z bit is clear (a result was non-zero or a comparison was not equal), then the branch will be taken.

## Slide 12: Conditional Branches
  MOV r0, #5 ; use r0 as loop counter, set to 5
  loop ; label indicating the start of the loop
  ... ; body of loop
  ...
  SUB r0, r0, #1 ; decrement loop counter, r0=r0-1
  CMP r0, #0 ; compare value in r0 and zero
  BNE loop ; if comparison was not equal, jump ; back to the “loop” label
  ... ; instructions after end of the loop

## Slide 13: Conditional Branches
MOV r0, #5 ; use r0 as loop counter, set to 5
  loop ; label indicating start of the loop
  ... ; various instructions (the loop body)
  ...
  SUBS r0, r0, #1 ; decrement loop counter (r0=r0 -1)
  ; and set the flags based on the ; subtraction result
  BNE loop ; if the Z bit is clear (i.e. "0"), jump
  ; back to “loop” label and repeat
  ... ; instructions after the loop's end

## Slide 14: Conditional Branch Instructions
ARM assembly has 16 conditional branches:
  including "always" (an unconditional branch)
  and "never" (which is never used but exists for future possible extensions to the architecture)

## Slide 15: Conditional Branch Instructions: 1
Branch | Condition Test | Meaning | Uses
B | No test | Unconditional | Always take the branch
BAL | No test | Always | Always take the branch
BEQ | Z=1 | Equal | Comparison equal or zero result
BNE | Z=0 | Not Equal | Comparison not equal or non-zero result
BCS | C=1 | Carry Set | Arithmetic operation gave carry out
BCC | C=0 | Carry Clear | Arithmetic operation did not produce a carry

## Slide 16: Conditional Branch Instructions: 2
Branch | Condition Test | Meaning | Uses
BHS | C=1 | Higher or same | Unsigned comparison gave higher or same result
BLO | C=0 | Lower | Unsigned comparison gave lower result
BMI | N=1 | Minus | Result is minus or negative
BPL | N=0 | Plus | Result is positive (plus) or zero
BVS | V=1 | Overflow Set | Signed integer operation: overflow occurred
BVC | V=0 | Overflow Clear | Signed integer operation: no overflow occurred

## Slide 17: Conditional Branch Instructions: 3
Branch | Condition Test | Meaning | Uses
BHI | ((NOT C) OR Z) =0 {C set and Z clear} | Higher | Unsigned comparison gave higher
BLS | ((NOT C) OR Z) =1 {C set or Z clear} | Lower or same | Unsigned comparison gave lower or same
BGE | (N EOR V) =0 {(N and V) set or (N and V) clear} | Greater or Equal | Signed integer comparison gave greater than or equal
BLT | (N EOR V) =1 {(N set and V clear) or (N clear and V set)} | Less Than | Signed integer comparison gave less than

## Slide 18: Conditional Execution
All instructions in ARM assembly can be conditionally executed
CMP r0, #10 ; compare the value in r0 with the value 10
BEQ jumpaway ; if the condition code indicates an equal ; comparison, branch to the jumpaway label
ADD r1, r1, r0 ; add the value in r0 to r1 and store the ; result in r1
SUB r2, r2, r0 ; subtract the value in r0 from r2 and store t ; the result in r2
Jumpaway … ...

## Slide 19: Conditional Execution
This can be rewritten as:
CMP r0, #10 ; compare the value in r0 with the value 10
ADDNE r1, r1, r0 ; add the value in r0 to r1 and store the result ; in r1
SUBNE r2, r2, r0 ; subtract the value in r0 from r2 and store the ; result in r2
... ; other code now follows
ADDNE and SUBNE are executed only if the Z bit is "0" (CMP had non-zero result, cleared Z)
Efficient if the conditional sequence is only three or less instructions; for longer sequences, use proper loops and conventional branching.

## Slide 20: Conditional Execution
The "S" suffix can be appended to instructions with the conditional suffices, enabling them to adjust the condition codes.
This can lead to unexpected behaviour
Let r0 be 4, r1 be -4, and r2 be 7
CMP r0, #10 ; compare the value in r0 with the value 10
; Z is 0
ADDNES r1, r1, r0 ; r0 ≠10, so Z is 0, so r1 = -4 + 4 is executed, ; and Z is now set
SUBNE r2, r2, r0 ; Z is already set (i.e. "1"), so SUBNE is not ; executed
... ; other code now follows

## Slide 21: Conditional Execution: 1
The conditional suffix mnemonics are the same as for conditional branches
Suffix | Condition Test | Meaning
EQ | Z=1 | Equal
NE | Z=0 | Not Equal
CS | C=1 | Carry Set (Unsigned Higher or Same)
CC | C=0 | Carry Clear (Unsigned Lower than)
MI | N=1 | Minus
PL | N=0 | Plus

## Slide 22: Conditional Execution: 2
Suffix | Condition Test | Meaning
VS | V=1 | Overflow Set
VC | V=0 | Overflow Clear
HI | ((NOT C) OR Z) =0 {C set and Z clear} | Higher unsigned
LS | ((NOT C) OR Z) =1 {C set or Z clear} | Lower or same unsigned
GE | (N EOR V) =0 {(N and V) set or (N and V) clear} | Greater or Equal
LT | (N EOR V) =1 {(N set and V clear) or (N clear and V set)} | Less Than
GT | (Z OR (N EOR V)) =0 {((N and V) set or clear) and Z clear} | Greater Than
LE | Z OR (N EOR V)) = 1 {(N set and V clear) or (N clear and V set) or Z set} | Less or Equal