## Slide 1
ARM Assembly

## Slide 2
Write down the steps in English
Then translate them into assembly commands

## Slide 3
<space>ADD a, b, c <tab> ; comment
There is a space before each command
Comments are optional

## Slide 4
AREA <name>, CODE, READONLY
ENTRY
start
<code>
<more code>
SWI 0x11
END

## Slide 5
Registers hold numbers (integers)
Negative values are stored in two's complement

## Slide 6
Two's Complement
Positive values are stored as usual.
Negative values:
Find the value as a positive number
Flip all the bits
Add 1
Negative numbers always start with a one on the left.

## Slide 7
MOV
MOV r1, #0

## Slide 8
ADD and SUB
ADD r0, r0, #1

## Slide 9
no multiply, no divide

## Slide 10
How would you multiply two numbers?

## Slide 11
2 x 4
2 + 2 + 2 + 2

## Slide 12
2 x 4 in assembly
AREA multiply, CODE, READONLY
ENTRY
start
MOV r0, #0
ADD r0, r0, #2
ADD r0, r0, #2
ADD r0, r0, #2
ADD r0, r0, #2
END

## Slide 13
How would you do 2 x 100?

## Slide 14
2 x 100
Set a total at 0
Set a counter at 0
Set number1 set to 2
Set number2 set to 100
Add number1 to the total
Add 1 to the counter
Repeat until the counter is equal to number2
The total now equals 200
Total goes up by 2, then 4, 6, 8, 10, 12 etc
Counter goes up by 1 each time

## Slide 15
2 x 100 in assembly
AREA multiply, CODE, READONLY
ENTRY
start
MOV r0, #0
MOV r1, #0
MOV r2, #2
MOV r3, #100
loop
ADD r0, r0, r2
ADD r1, r1, #1
CMP r1, r3
BNE loop
END

## Slide 16
?

## Slide 17
LDR and STR
load and store
LDR <value>, <target address>